## Slide 1: Modeling Wave Propagation: On-body & In-body Communication
Zbyněk Raida
raida@vut.cz
Body-centric wireless communication
Vytvořeno za podpory projektu OP VVV Moderní a otevřené studium techniky CZ.02.2.69/0.0/0.0/16_015/0002430

## Slide 2: Recap
Why phantoms are exploited?
What kinds of phantoms are known, and when are they used?
How the specific absorption rate (SAR) is defined, and what are the admissible limits?
How does the layered phantom look like? How do its parameters vary with frequency?
Why phantoms have to be calibrated and what is the calibration procedure?

## Slide 3: Wired  wireless communication
Can be human body represented by a conductive ground plane?

## Slide 4: Tissue parameters
 | d [mm]
Skin | 2
Fat | 10
Muscle | 28
2.4 GHz | r [-] |  [S/m]
Skin | 38.063 | 1.441
Fat | 5.285 | 0.102
Muscle | 52.791 | 1.705

## Slide 5: Tissue parameters
5.8 GHz | r [-] |  [S/m]
Skin | 35.114 | 3.717
Fat | 4.955 | 0.293
Muscle | 48.485 | 4.962
60 GHz | r [-] |  [S/m]
Skin | 7.975 | 36.39
Fat | 3.132 | 2.815
Muscle | 12.856 | 52.82

## Slide 6: Wired communication
Immunity against interferences
High efficiency
  Propagation of EM energy in a single direction
  Losses in dielectrics
  Losses in inner conductor and shielding
Applicable in case of on-body communication only

## Slide 7: Wired communication

## Slide 8: Wireless communication
High mobility
High sensitivity to interferences
Low efficiency
  Energy propagation in all directions
  Losses in surrounding (tissues heated)
  Losses in an antenna
Necessary when communicating in a body or off a body

## Slide 9: Contents
Efficiency of wireless communication
Off-body communication free-space propagation (air)
In-body communication wave propagation in a lossy environment (inhomogeneous)
On-body communication wave propagation along the interface of a lossy environment and the air

## Slide 10: Efficiency
Coaxial line: 6 dB / 100 m  P2 = 0.25 P1
Free space: Friis equation
Reception and transmission by half-wavelength dipoles (gain G = 1.64), frequency f = 2.0 GHz and the distance R = 100 m

## Slide 11: Efficiency
Symmetric dipole: 75 dB / 100 m  P2 = 108 P1
effective aperture
surface of wavefront
Transmission: P2 = 101 P1

## Slide 12: Off-body propagation
Propagation in a half-space  reflector
Forward and reflected wave in phase:  Etot = 2E  Ptot = +6 dB

## Slide 13: Off-body propagation
Wave equations
where

## Slide 14: Off-body propagation
In general:
attenuation constant
phase constant

## Slide 15: Off-body propagation [vacuum]
Negligible losses

## Slide 16: An example: magnetic loop
LÁČÍK, J. Circularly polarized SIW square ring-slot antenna for X-band applications, Microwave and Optical Technology Letters, 2012, vol. 54, no. 11, p. 2590-2594.
Gain Theta

## Slide 17: An example: magnetic loop
LÁČÍK, J. Circularly polarized SIW square ring-slot antenna for X-band applications, Microwave and Optical Technology Letters, 2012, vol. 54, no. 11, p. 2590-2594.
Reflection coefficient
Fabricated antenna
Reflection coefficient (dB)

## Slide 18: In-body propagation [dielectrics]
phase velocity
wavelength
power density
wave impedance

## Slide 19: An example: wireless endoscopy
Sensor capsule in digestive tract, receive antenna on body surface
SUZAS MIAH, Md., et al. Antenna system design for improved wireless capsule endoscope links at 433 MHz. IEEE Transactions on Antennas and Propagation, 2019, vol. 67, no. 4, p. 2687-2699.

## Slide 20: An example: wireless endoscopy
f1 = 433 MHz  f2 = 2.4 GHz
RAŠKA, M. Sensing the sensor signal in digestive tract. Bachelor thesis. Brno University of Technology, 2019.

## Slide 21: On-body propagation
On-body communication
EM energy radiated into a half-space:  half value of radiation resistance  Ptot = +3 dB

## Slide 22: On-body propagation
Perfect electric conductor (PEC)  lossy dielectrics
Norton wave
space wave
direct
reflected
J. C. Jordan, K. G. Balmain, Electromagnetic Waves and Radiating Systems, Englewood Cliffs: Prentice Hall, 1968.

## Slide 23: On-body propagation
Vertically polarized surface wave
kde
wave number
numeric distance
complex permittivity
distance between antennas

## Slide 24: On-body propagation
Attenuation function
where
Approximation for p > 20

## Slide 25: On-body propagation

## Slide 26: ISM band 60 GHz
planar equivalent phantom comprising diffraction

## Slide 27: Phantom 60 GHz
Reflection coefficient at the input of quarter-wavelength monopole

## Slide 28: Phantom 60 GHz
Tuning parameters [, ] of Norton model: comparison of transmission coefficient with voxel model

## Slide 29: An example: horn antenna
CUPAL, M.; RAIDA, Z. H-plane SIW horn antenna for on-body communication. Radioelektronika 2016. Košice (Slovakia): IEEE. DOI: 10.1109/RADIOELEK.2016.7477347

## Slide 30: An example: horn antenna
CUPAL, M.; RAIDA, Z. H-plane SIW horn antenna for on-body communication. Radioelektronika 2016. Košice (Slovakia): IEEE. DOI: 10.1109/RADIOELEK.2016.7477347

## Slide 31: An example: horn antenna
CUPAL, M.; RAIDA, Z. H-plane SIW horn antenna for on-body communication. Radioelektronika 2016. Košice (Slovakia): IEEE. DOI: 10.1109/RADIOELEK.2016.7477347

## Slide 32: Summary
Wired versus wireless communication: the problem of efficiency
Electrical parameters of human body: in-body / off-body / on-body wave propagation
On-body communication: Norton wave
Increasing frequency  the increase of attenuation