## Slide 1: Wireless Body-centric Area Networks: Examples
Zbyněk Raida
raida@vut.cz
Body-centric wireless communication
Vytvořeno za podpory projektu OP VVV Moderní a otevřené studium techniky CZ.02.2.69/0.0/0.0/16_015/0002430

## Slide 2: Example #1
Bluetooth-based Wireless Body Area Network (WBAN)
The 24th International Traveling Summer School on Microwaves and Lightwaves
Copenhagen (Denmark), July 2014
Jan Velim, Brno University of Technology Leonardo Di Alessandro, Tor Vergata University, Rome Tomasz Karpisz, Warsaw University of Technology José Estarán, Technical University of Denmark

## Slide 3: WBAN

## Slide 4: WBAN

## Slide 5: WBAN
Wireless Body Area Network (WBAN) - ISM regulations (2.4 GHz  5.8 GHz band) - Sensors, central unit and remote node - Medical / sport applications

## Slide 6: WBAN
Design challenges: - Central unit - Sensing network - Antenna - Interfacing the remote node - Power feeding

## Slide 7: Case analysis
Reliable - Single central unit (CU) ensures the proper function of the network
Scalable / flexible - Complex network design (interfacing CU and remote node)
Cheap - Wireless link with intermediate access / interface

## Slide 8: Case analysis
Low power consumption - Power-efficient data communication protocols
Compatible with remote devices - ISM frequency bands preferred
Minimum number of invasive elements - Ideally, only the on-body sensors (epidermal electronics)

## Slide 9: The system
Optimum 10 m reach at 1 Mbps
Low power consumption <15 mA
Point-multipoint (max 7 devices)
Automatic synchronization
Cheap and rapid implementation
ISM band 2.4 GHz with 100 MHz modulation BW

## Slide 10: Sensors
Humidity: STN21
Supply Voltage, VDD
Power Dissipation
0.5 µW (sleep mode)
3 V
0.9 mW (measuring)
Operatin range
0 – 100 % RH
Output
I2C, 12 bit, 8 bit
Price
cca 3.5 €

## Slide 11: Sensors
Heart rate: Polar H7
200 h
3 V
Bluetooth
Supply Voltage, VDD
Battery lifetime
Communication
Price
cca 50 €

## Slide 12: Sensors
Accelerometer: LIS3DH
Supply Voltage, VDD
Current consumption
11 mA (norm. mode)
3 V
6 mA (Low P. mode)
 (2, 4, 8, 16) g dynamically selectable full scale
Output
I2C
Price
cca 1 €

## Slide 13: Sensors
Microphone: AKU230
Supply Voltage, VDD
Current consumption
1.2 mA (normal mode)
3 V
11 µA (low power mode)
Frequency Range
50 Hz – 22 kHz
Signal to Noise Ratio
56 dB
Sensitivity
-26 dBFS

## Slide 14: Transceiver
Supply Voltage, VDD
Current consumption
3 V
15.7 mA (Receiv.)
Interface
I2C
Price
cca 10 €
12.6 mA (Trans.)
Transmit Power
0 dBm
Receiver Power
-94 dBm
TiWi: uB1

## Slide 15: Power Supply
Button battery: CR2025
Nominal Voltage
Nominal Capacity
3 V
160 mAh
Average weight
2.4 grams
Price
cca 1 €

## Slide 16: Power Supply
Shoe generator
Available Power
Transmit Energy
Upto 20 W
Bluetooth
Principle
Electroswetting
Price
cca ?? €

## Slide 17: Antenna
PCB antenna
2.4 GHz / 100 MHz BW
Matched at 50 
Size: 15.2  5.7 mm

## Slide 18: Antenna
PCB antenna
Audun Andersen, Small size 2.4 GHz PCB antenna, Application Notes, AN043.

## Slide 19: Summary
Simple WBAN composed from commercially available components equipped with Bluetooth interface
Low price
Easy to develop, easy to use
Customizable: sensors to be selected on demand

## Slide 20: Example #2
Wireless Body Area Network (WBAN) for Animals
The 25th International Traveling Summer School on Microwaves and Lightwaves
Madrid (Spain), July 2015
Luca Liberati, University of L'Aquila Vytautas Jakstas, Center for Physical Science & Technol. Till Mohr, Technische Universität Darmstadt Mahsa Ebrahimpouri, KTH Stockholm

## Slide 21: Motivation
Losses of cows in the UK caused by diseases:
4.5 million incinerated due to bovine spongiform encephalopathy in 1986;
4.0 million slaughtered due to foot and mouth disease;
In total, economic losses 13 billion ₤.

## Slide 22: Motivation
Detect diseases at an early stage
Additional: reduction in the required amount of medicine.

## Slide 23: Requirements
Cheap
Comfortable
Reliable
Easy to mount and use
Long-life time
Weather resistant (waterproof etc.)
Self powering
Weak back radiation of antennas

## Slide 24: Concept
Several sensors attached to animal body
Each sensor transmits data to base unit
Base unit stores data
Reaching the feeding place, the base unit transmit data to computer.

## Slide 25: Energy harvesting
Solar cell
Integrated into animal’s belt.
Powering energy extensive sensors and communication systems.
Flexible solar cells provide up to 1 W (size 10 x 19.8 cm)

## Slide 26: Energy harvesting
Pyroelectric source
Pyroelectric energy harvesting needs change of temperature.
The temperature of cow changes over 1°C.
An average harvesting: 1µW/cm2 on 100 µm thick device.
[1] R. H. Watson, Georgia Automated Environmental Monitoring Network, The University of Georgia, USA
[2] G. Sebald et al., Smart Material Structures, 18 (2009)
Steer body temperature measured every 15 minutes during a warm day

## Slide 27: Sensors
Body temperature
[1] R. Ch. Webb, Nature Materials 12, 938–944 (2013)

## Slide 28: Sensors
Heart beating
Commercially available
Open source hardware
Small size

## Slide 29: Sensors
Blood pressure
Uses cheap LED & PD

## Slide 30: Sensors
Breathing
Simple thermistor attached to nose stud [1]
Exhaling changes the temperature
[1] http://www.datasci.com

## Slide 31: Sensors
Movement (GPS)
Attached to base unit.
Commercially available
Quick on/off to save energy
[1] http://www.trimble.com

## Slide 32: Antennas

## Slide 33: Antennas
Impedance matching

## Slide 34: Antennas
Radiation patterns

## Slide 35: Antennas
Back radiation

## Slide 36: Antennas
Body effect
animal fur

## Slide 37: Antennas
Experimental results

## Slide 38: Antennas
Experimental results
flat antenna
curved antenna (r = 100 mm)

## Slide 39: Summary
Autonomous cow healthcare monitoring
Energy harvesting by solar cells and pyroelectrics
Sensing temperature, heart-beat, blood pressure, breathing
Off-body communication by circular patch antenna